## Slide 1: Cache Hierarchy Optimizations for Graph Analytics
CS230: Digital Logic Design & Computer Architecture
Karan Godara (210050082)
Isha Arora (210050070)
Shantanu Welling (210010076)

## Slide 2: Baseline Configuration
CACHE | CONFIGURATION
L1 I-CACHE | 64 SET, 8 WAY
L1 D-CACHE | 64 SET, 12 WAY
L2 CACHE | 1024 SET, 8 WAY
LAST LEVEL CACHE | 2048 SET, 16 WAY
Traces Used : sssp-14 and bfs-14
Base replacement policy : LRU
No prefetcher for all cache levels in Base configuration

## Slide 3: Data Types in Graph Traces
Structure data: the neighbor ID array.
Property data: the vertex data array
Intermediate data: any other data.

## Slide 4: Baseline Results
L1D Miss Rate: 13.66%
L2C Miss Rate: 58.88%
LLC Miss Rate: 90.56%
IPC: 0.1697
L1D Miss Rate: 22.06%
L2C Miss Rate: 61.64%
LLC Miss Rate: 34.56%
IPC: 0.2909
BFS Trace SSSP Trace

## Slide 5: Shall we increase the cache size?
L2C Size ↑↑ IPC No Change ☹

## Slide 6: What about LLC😲? Any Hopes?
LLC Size ↑↑ IPC ↑↑
Increasing L2C size doesn't affect IPC significantly, but increasing LLC size shows a significant increase in IPC
Reuse distance either very short or very long

## Slide 7: Maybe change cache hierarchy?
Clearly non-inclusive cache hierarchy performs better for graph analytics than exclusive or inclusive cache hierarchy on a single core processor

## Slide 8: So what to do now?
How to make sure reused data stays in the cache? How to increase the hit-rate of caches?
Attempt-> Use better replacement policies 🤩
How to utilize L2C effectively?
Attempt-> Use prefetchers 🤩

## Slide 9: Replacement policies
What are our options now?
Heuristic Policies | Non-Heuristic Policies
Most Recently Used (MRU) | Signature based Hit Predictor (SHIP)
First In First Out (FIFO) | Mockingjay
Least Frequently Used (LFU) | Hawkeye
Random | 
Least Recently Used (LRU) | 
Dynamic Re-Reference Interval Prediction (DRRIP) | 
Static Re-Reference Interval Prediction (SRRIP) | 

## Slide 10: Non-heuristic >>> Heuristic

## Slide 11: Where to prefetch?
L2 Cache:
No risk of cache pollution
Technique to make the under-utilized L2 cache useful

## Slide 12: Prefetchers
What are our options now???
Next Line Prefetcher
Berti: Local Delta Prefetcher
Signature Path Prefetcher (SPP)
T-Skid Prefetcher
5. Bouquet of Prefetchers (IPCP)
6. Sangam Prefetcher
7. Best Offset Prefetcher (BOP)
8. Pangloss

## Slide 13: ChampSim ChampSim on the wall, tell me which prefetcher is the best of them all?

## Slide 14: BOP Idea 1: Non-timely
Remove delay queue
BOP Idea 2: Fetch More
Increase prefetch degree

## Slide 15: BOP Idea 3: Multiple
Increase the number of candidate offsets tested per iteration
BOP Idea 4: Foresight
Increase prefetch distance

## Slide 16: The Winner : Fetch More

## Slide 17: Best config : BOP_FM in L2 & LLC

## Slide 18: Pangloss vs Improved BOP
Improved BOP_FM worked better 🤩

## Slide 19: Specializing Cache Replacement Policies for Graph Analytics
A person who never made a mistake, never tried anything new. Sounds familiar?

## Slide 20: Improving Hawkeye
#Idea 1
Changed the way hawkeye deals with absence cache averse line
Tried using FIFO, LFU instead of the default LRU that Hawkeye uses

## Slide 21: Improving Hawkeye
#Idea 2
Tried reducing memory traffic
Treated demand and prefetch access the same for determining the Bellady cache occupancy

## Slide 22: Failure quantified!!

## Slide 23
Biswa:

## Slide 24: Improving Hawkeye
#Idea 3
Increasing cache associativity
Changed LLC associativity while keeping cache size constant

## Slide 25: It works!!

## Slide 26: Future prospect
Prefetch aware non-heuristic policies in the absence of cache averse lines are expected to perform better

## Slide 27: Ruko zara! Sabar karo! We aren't done yet Optimizations in Mockingjay ahead
# Idea 1:
Changing Penalty Factor
Ignore redundant prefetches to maximize cache utilization

## Slide 28: Penalty Factor Variation Results

## Slide 29: Optimizations in Mockingjay
# Idea 2 :
Increasing eviction priority of blocks with largest ETR (Estimated Time Remaining)
Decreased MAX_RD

## Slide 31: Future prospect
Changing prefetch granularity
Different kind of adaptive miss filter ( hit filter/ time-based filter)

## Slide 32: Now, comparing the best among the two
Optimized Mockingjay performed better than hawkeye

## Slide 33: Comparing prefetchers
It is trace dependent. BOP_FM performed better for BFS trace whereas Pangloss performed better for SSSP trace

## Slide 34: Thankyou Biswa and the TAs☺ We bid adieu to this amazing course ☹